## Slide 1: IMU Pose Reconstruction
Analysis of KITTI Drive 2011_09_30_0020

## Slide 2: Objective & Data Source
Goal: Reconstruct 3D vehicle trajectory using IMU data and fuse with visual data.
Dataset: KITTI Odometry (2011_09_30_drive_0020_sync).
Input Data:
- Accelerometer (ax, ay, az)
- Gyroscope (wx, wy, wz)
- Timestamps (converted to delta_t)

## Slide 3: Methodology: Error-State EKF
Architecture: Nominal State (Kinematics) + Error State (Noise).
State Vector:
- Position (p), Velocity (v), Orientation (q)
- Biases (b_acc, b_gyro)
Prediction Loop:
1. Integrate Angular Rate -> Update orientation (Quaternion)
2. Rotate Accel to World Frame
3. Integrate Accel -> Velocity -> Position

## Slide 4: Key Challenge: Gravity Compensation
IMU measures Specific Force, not acceleration.
We must subtract gravity in the World Frame:
a_world = (R * f_body) - G_world
Crucial Dependency:
If Orientation (R) is wrong, Gravity is subtracted incorrectly.
This leaves wrong acceleration on X/Y axes.

## Slide 5: The 'Straight Line' Drift Issue
Observation: Trajectory does not follow the ground truth of being a straight line with 180 degree turn from time to time.
Possible Causes: Initialization Error, Consistent drift in acceleration
- Initialized with q=[0,0,0,1] (Identity).
- Failed to account for initial vehicle Pitch/Roll.
Result: A massive constant false acceleration masked the true turning motion.

## Slide 6: Solution: Static Initial Alignment
Method: Calculate q0 using first IMU frame.
Roll (phi) = atan2(-ay, az)
Pitch (theta) = atan2(ax, sqrt(ay^2 + az^2))
Yaw (psi) = Obtained from OXTS heading.
Outcome: Corrected the Gravity Vector alignment, revealing true motion direction.

## Slide 7: Results
[PLACEHOLDER: trajectory plot here]
- Blue line: EKF Prediction

## Slide 8: Conclusion
Implemented ES-EKF prediction step.
Validated that correct Attitude Initialization is critical for INS accuracy.
Next steps
Update the pose from Visual Odometry.
Test SIFT features and compare with Shi-Tomasi